## Slide 1
COMPUTER ORGANIZATION & ARCHITECTURE | B.TECH · YEAR 1
4-Bit ALU Architecture
and Components
From binary logic to a RISC-V processor datapath
INPUTS
A[3:0], B[3:0]
ALU
Arithmetic + Logic
CONTROL
Operation select
OUTPUT
F[3:0] + flags
→
→
→
01
PRESENTED BY
Harshini — 2620080087 | Bhavya — 2620030582
Raghavendra — 2620030549 | Sreevalli — 2620030535
KL UNIVERSITY BACHUPALLY

## Slide 2
01 · CO1
Computer organization and binary data
The ALU is one part of the CPU, and binary values are the data it processes.
02
Basic computer blocks
Input → CPU ↔ Memory → Output
CPU includes the ALU, Control Unit, and registers.
4-bit representation
A 4-bit unsigned value ranges from 0 to 15.
Example: 1010₂ = 10₁₀
Logic gates
AND, OR, NOT, and XOR process bits.
Gate outputs form the logic section of an ALU.
Example 4-bit word
1
0
1
0
MSB LSB
Most significant Least significant

## Slide 3
02 · CO2
4-bit ALU architecture and components
Combinational circuits calculate candidate results; a multiplexer selects one result.
03
A[3:0]
B[3:0]
→
ARITHMETIC
Adder / subtractor
(full-adder stages)
LOGIC
AND · OR · XOR · NOT
→
MUX
Select result
→
F[3:0]
Status flags*
Control Unit → operation-select lines
*Flags depend on the design. Common examples: Carry and Zero; signed designs may also track Negative and Overflow.

## Slide 4
02 · CO2
Arithmetic and logic operations
This example uses a 2-bit operation selector; the chosen design supports four core operations.
04
S1 S0
Operation
Example (A = 1010, B = 0011)
F
0 0
AND
1010 AND 0011
0010
0 1
OR
1010 OR 0011
1011
1 0
ADD
1010 + 0011
1101
1 1
SUB
1010 − 0011
0111
Addition
1010₂ (10) + 0011₂ (3) = 1101₂ (13)
Subtraction
1010₂ (10) − 0011₂ (3) = 0111₂ (7)

## Slide 5
03 · CO3
Sequential logic: storing and moving data
Combinational logic calculates; sequential logic remembers state using clocked storage.
05
Flip-flops
Store one bit. Common types include D and JK flip-flops.
A clock coordinates when state changes.
Registers and shift registers
A register stores a multi-bit value. A shift register moves bits left or right on clock events.
Counters, PC and FSMs
Counters track steps; the Program Counter stores the next instruction address; an FSM controls state transitions.
Operand register
4-bit ALU
Result register
→
→
Clocked registers make it possible to use the ALU repeatedly across synchronized processor steps.

## Slide 6
04 · CO4
Register file and memory hierarchy
The ALU reads operands from registers and sends its result back to the datapath.
06
REGISTER FILE
Read rs1 and rs2
Write rd
4-BIT ALU
Arithmetic or
logic operation
WRITE-BACK
Result returns
to destination
→
→
Memory hierarchy (generally fastest to slowest)
Registers
Very small, fastest CPU storage
Cache
Keeps frequently used data close to CPU
RAM
Main memory for active programs and data
Storage
Persistent SSD / hard-drive storage
The ALU computes values; memory and register structures supply, store, and transfer them.

## Slide 7
05 · CO5
RISC-V instructions and ALU datapath
RISC-V instructions use control signals to guide data through the processor.
07
IF
Fetch instruction
→
ID
Decode + read registers
→
EX
ALU executes
→
MEM
Access data memory if needed
→
WB
Write result back
Example: ADD
add x3, x1, x2
If x1 = 10 and x2 = 3, then x3 = 13.
Other ALU roles
Calculate load/store addresses and compare values for branch decisions. The 4-bit design is a learning model; common RISC-V implementations use 32-bit datapaths.
Note: this slide shows the classic five-stage instruction path for explanation. A single-cycle implementation completes an instruction in one clock cycle rather than using five separate pipeline stages.

## Slide 8
05–06 · CO5 + CO6
Single-cycle processor and architectural extensions
A simplified datapath connects instruction control, the ALU, registers, memory, and peripherals.
08
PC
Instruction address
Instruction memory
Fetch instruction
Control unit
Generate control signals
Register file
Read / write operands
ALU
Execute / address
Data memory
Load / store
Write-back MUX
Choose result
→
→
↓
←
←
←
Possible extensions (CO6)
• Add XOR, shifts, flag logic, wider datapaths, and interfaces to timers, sensors, or other peripherals.
• A single-cycle design completes each instruction in one cycle; the clock period must cover the slowest instruction path.

## Slide 9
06 · CO6
Simulation, verification and project learning
Test the expected result of each operation before integrating the ALU into a processor.
09
Operation
A
B
Expected F
AND
1010
0011
0010
OR
1010
0011
1011
ADD
1010
0011
1101
SUB
1010
0011
0111
How to verify
Build in Logisim Evolution; test every select code and compare outputs.
Project extension
Connect registers, control signals, and a simple peripheral interface; document test cases and results.

## Slide 10
THANK YOU
Questions & Discussion
4-Bit ALU Architecture and Components · CO1–CO6